## Slide 1
Iot_curtain_call
PROJECT
Smart Home · WhatsApp · IPX800 V4
‹
›

## Slide 2
System Architecture
Smart Home · WhatsApp Control
WhatsApp
Meta Cloud API
Node.js Webhook
HTTPS :443 · VPS
FastAPI Service
HTTP :8000 · VPS
IPX800 V4
Home LAN · DDNS
HTTPS POST
HTTP :8000
DDNS :8080
VPS
VPS (Public): Node.js :443 + FastAPI :8000 Home LAN: IPX800 via DDNS + port-forward :8080

## Slide 3
Call Flow — WhatsApp → Relay
End-to-end message sequence
User
WhatsApp
Meta API
Cloud API
Node.js
:443 VPS
FastAPI
:8000 VPS
IPX800 V4
Home LAN
▶
"light on"
▶
POST /webhook HTTPS
◁
HTTP 200 (immediate)
HMAC · whitelist · dedup
▶
POST /control (loopback)
LIGHT_ON → relay 1
▶
GET /preset.htm?led1=1
relay 1 closes ✓
◁
200 OK
◁
{"reply":"✅ Light ON"}
▶
POST /messages Graph API
◁
"✅ Light turned ON"
3 / 7

## Slide 4
Curtain Interlock Safety
Motor protection · relay sequencing
⚠️ Simultaneous UP + DOWN signals would burn the motor windings — software interlock is mandatory.
❌ Without interlock
relay 2 (UP) = ON
relay 3 (DOWN) = ON
→ Motor stall / burnt windings
✅ With interlock
relay 3 (DOWN) = OFF ← clear
sleep(200 ms) ← gap
relay 2 (UP) = ON ← set
Relay mapping: R1 = Light · R2 = Curtain UP · R3 = Curtain DOWN

## Slide 5
Security Layers
Defence-in-depth · 6 independent mechanisms
🔐 Transport
TLS 1.2/1.3 · Let's Encrypt · Node.js terminates
✍️ Authenticity
HMAC-SHA256 on every Meta POST · verifySignature()
📋 Authorization
Phone whitelist E.164 · unknown senders dropped
🔁 Replay protection
Last-200 message-ID dedup · reprocessing blocked
🔒 Internal isolation
FastAPI binds 127.0.0.1:8000 · never public
⚙️ Motor safety
Software interlock + 200 ms gap · ipx800.py

## Slide 6
Setup Checklist
Pre-deployment · fill .env → smoke test
VPS Infrastructure
Static public IP + domain A record
Let's Encrypt cert (privkey + fullchain)
Port 443 inbound · port 8000 loopback only
IPX800 V4
API key set in Settings → API
Relay wiring: R1=Light R2=UP R3=DOWN
DDNS configured (DuckDNS / No-IP)
Port forward TCP 8080 → IPX800:80
Meta / WhatsApp
Meta Developer account + Business app
WA_PHONE_NUMBER_ID + permanent token
WA_APP_SECRET from App Settings → Basic
Webhook registered · field: messages
Environment variables
webhook/.env: phone ID, token, secret, verify, numbers
fastapi/.env: IPX800_HOST, PORT, APIKEY
Smoke test: curl http://127.0.0.1:8000/health

## Slide 7
Ready to Deploy
Fill .env → start services → register Meta webhook → send "light on"
Node.js :443
FastAPI :8000
IPX800 via DDNS
IPX800 V4 Smart Home — WhatsApp Control System